## Slide 1: Rocket Motors

## Slide 2: How Engines Work
In order for something to burn, you need a fuel + oxidizer
  Fuel – the chemical that burns
  Oxidizer – the thing that causes the burning
Compare this to airplanes
  Where is their oxidizer?
Motor vs engine
Notes: Motor is simple device that stores propellant, engine is more complicated with moving parts to convert stored propellant into thrust

## Slide 3: Airplane Motors
Notes: Turboprop: Normal engine drives a propeller, the propeller propels air back, generating thrust
Turbojet engine: Air gets intake, compressed, fuel added, burned, and then expelled
Ramjet: Air gets compressed due to the aircraft going a high speed – aircraft using it normally need assistance to get up to speeds because ram jets have low efficiency at low speeds
All 3 work by expelling air backwards

## Slide 4: Rocket Propulsion
Solid Fueled Rockets
Liquid Fueled Rockets
Hybrid Rockets
Notes: Have students guess which ones

## Slide 5: Solid Propulsion
Easy to store and handle
Compact
Unable to control throttle
Manufacturing precision
Notes: Used in space shuttle booster stages
Tiniest defects can be catastrophic in the motor, such as voids or cracks

## Slide 6: Liquid Propulsion
Complex
Able to be throttled
Hard to store
Higher thrust compared to solid fuel
Notes: Complex – lots of valves and throttling control systems
Hard to store – liquid hydrogen is very small, seeps into cracks easily, has to be kept at extremely low temperatures
Hybrid rockets – pretty rare, typically uses solid fuel and liquid oxidizer

## Slide 7: Core Burning vs End Burning
Notes: However, to get higher thrust, the hollow core is used. This increases the surface area of the propellants available for burning. The propellants burn from the inside out at a much higher rate, sending mass out the nozzle at a higher rate and speed. This typically results in greater thrust.
End burning – easier to manufacture, longer burn time, but can lift less payload

## Slide 8: Chemical Reactions
Combustion:
  Liquid hydrogen + liquid oxygen
  Gunpowder
  Alcohol + Oxygen
Acid/base:
  Baking soda + vinegar
  Alka seltzer + water
Notes: Liquid hydrogen and oxygen combine to turn into water, releasing energy and hot gasses that get expelled, producing thrust
Gunpowder – charcoal is fuel, potassium nitrate is oxidizer
Baking soda + vinegar produce CO2, and that gas gets expelled, producing thrust
Alka seltzer contains both the base and the acid – citric acid and sodium bicarbonate ( baking soda) – water is just a catalyst – reaction also releases CO2